## Slide 1: ModelSim Demo
Sequential Circuit

## Slide 2: Master slave d flip flop

## Slide 3
clk
d
rst
clk
d
rst
q
qbar
q
qbar
q
qbar
d
rst
clk

## Slide 4: Master slave flip flop

## Slide 5: D- flip flop
module dff_sync_reset (data , clk , reset , q );
//-----------Input Ports---------------
input data, clk, reset ;
//-----------Output Ports---------------
output q;
//------------Internal Variables--------
reg q;
//-------------Code Starts Here---------
always @ ( posedge clk)
if (~reset) begin
q <= 1'b0;
end else begin
q <= data;
end
endmodule //End Of Module dff_sync_reset

## Slide 7: An 4-bit synchronous counter

## Slide 8
module first_counter (clock , // Clock input of the design
reset , // active high, synchronous Reset input
enable , // Active high enable signal for counter
counter_out // 4 bit vector output of the counter
); // End of port list
//-------------Input Ports-----------------------------
input clock ; input reset ; input enable ;
//-------------Output Ports----------------------------
output [3:0] counter_out ;
//-------------Input ports Data Type-------------------
// By rule all the input ports should be wires
wire clock ; wire reset ; wire enable ;
//-------------Output Ports Data Type------------------
// Output port can be a storage element (reg) or a wire
reg [3:0] counter_out ;

## Slide 9
//------------Code Starts Here-------------------------
// Since this counter is a positive edge trigged one, We trigger the below block with respect to positive edge of the clock.
always @ (posedge clock)
begin : COUNTER // Block Name
// At every rising edge of clock we check if reset is active . If active, we load the counter output with 4'b0000
if (reset == 1'b1) begin
counter_out <= #1 4'b0000;
end
// If enable is active, then we increment the counter
else if (enable == 1'b1) begin
counter_out <= #1 counter_out + 1;
end
end // End of Block COUNTER
endmodule // End of Module counter

## Slide 10: Counter Test Bench

## Slide 11
`include "first_counter.v"
module first_counter_tb();
// Declare inputs as regs and outputs as wires
reg clock, reset, enable;
wire [3:0] counter_out;
// Initialize all variables
initial begin
$display ("time\t clk reset enable counter");
$monitor ("%g\t %b %b %b %b",
$time, clock, reset, enable, counter_out);
clock = 1; // initial value of clock
reset = 0; // initial value of reset
enable = 0; // initial value of enable
#5 reset = 1; // Assert the reset
#10 reset = 0; // De-assert the reset
#10 enable = 1; // Assert enable
#100 enable = 0; // De-assert enable
#5 $finish; // Terminate simulation
end

## Slide 12
// Clock generator
always begin
#5 clock = ~clock; // Toggle clock every 5 ticks
end
// Connect DUT to test bench
first_counter U_counter (
clock,
reset,
enable,
counter_out
);
endmodule

## Slide 14
# time clk reset enable counter
# 0 1 0 0 xxxx
# 5 0 1 0 xxxx
# 10 1 1 0 xxxx
# 11 1 1 0 0000
# 15 0 0 0 0000
# 20 1 0 0 0000
# 25 0 0 1 0000
# 30 1 0 1 0000
# 31 1 0 1 0001
# 35 0 0 1 0001
# 40 1 0 1 0001
# 41 1 0 1 0010
# 45 0 0 1 0010
# 50 1 0 1 0010
# 51 1 0 1 0011
# 55 0 0 1 0011
# 60 1 0 1 0011
# 61 1 0 1 0100
# 65 0 0 1 0100
# 70 1 0 1 0100
# 71 1 0 1 0101
# 75 0 0 1 0101
# 80 1 0 1 0101
# 81 1 0 1 0110
# 85 0 0 1 0110
# 90 1 0 1 0110
# 91 1 0 1 0111
# 95 0 0 1 0111
# 100 1 0 1 0111
# 101 1 0 1 1000
# 105 0 0 1 1000
# 110 1 0 1 1000
# 111 1 0 1 1001
# 115 0 0 1 1001
# 120 1 0 1 1001
# 121 1 0 1 1010
# 125 0 0 0 1010
# ** Note: $finish : G:/2014/TA_Jul_Dec/modelsim_into/271014/first_counter_tb.v(19)
# Time: 130 ps Iteration: 0 Instance: /first_counter_tb
Output of the $display and $monitor command

## Slide 15: Reference
1. A VERILOG HDL Primer, Second Edition, J.Bhasker